## Slide 1: Embedded System Design
Unit II
Typical Embedded System
Mr. A. Chandra Shaker
Asst. Prof

## Slide 2: Typical Embedded System
Unit II
Core of Embedded System
Memory
Sensors and Actuators
Communication Interface

## Slide 3: Typical Embedded System
      Memory
Memory is an important part of an embedded system. The memory used in embedded system can be either Program Storage Memory (ROM) or Data memory (RAM).
Certain Embedded processors/controllers contain built in program memory and data memory and this memory is known as on-chip memory.

## Slide 4: Typical Embedded System
      Memory – Program Storage Memory (ROM)
Stores the program instructions.
Retains its contents even after the power to it is turned off. It is generally known as Non volatile storage memory.
Depending on the fabrication, erasing and programming techniques they are classified into:

## Slide 5: Typical Embedded System
      Program Storage Memory – Masked ROM (MROM)
One-time programmable memory.
Uses hardwired technology for storing data.
The device is factory programmed by masking and metallization process according to the data provided by the end user.
The primary advantage of MROM is low cost for high volume production. They are the least expensive type of solid state memory.
The limitation with MROM based firmware storage is the inability to modify the device firmware against firmware upgrades. Since the MROM is permanent in bit storage, it is not possible to alter the bit information.
Different mechanisms are used for the masking process of the ROM.

## Slide 6: Typical Embedded System
      Program Storage Memory – Programmable Read Only Memory (PROM) / (OTP)
Unlike MROM it is not pre-programmed by the manufacturer.
PROM/OTP has nichrome or polysilicon wires arranged in a matrix, these wires can be functionally viewed as fuses.
It is programmed by a PROM programmer which selectively burns the fuses according to the bit pattern to be stored.
Fuses which are not blown/burned represents a logic “1” where as fuses which are blown/burned represents a logic “0”.The default state is logic “1”.
OTP is widely used for commercial production of embedded systems whose proto-typed versions are proven and the code is finalized.
It is a low cost solution for commercial production. OTPs cannot be reprogrammed.

## Slide 7: Typical Embedded System
      Program Storage Memory – Erasable Programmable Read Only Memory (EPROM)
Erasable Programmable Read Only (EPROM) memory gives the flexibility to re-program the same chip.
EPROM stores the bit information by charging the floating gate of an FET.
Bit information is stored by using an EPROM Programmer, which applies high voltage to charge the floating gate.
EPROM contains a quartz crystal window for erasing the stored information. If the window is exposed to Ultra violet rays for a fixed duration, the entire memory will be erased.
Even though the EPROM chip is flexible in terms of re-programmability, it needs to be taken out of the circuit board and needs to be put in a UV eraser device for 20 to 30 minutes.

## Slide 8: Typical Embedded System
      Program Storage Memory – Electrically Erasable Programmable Read Only Memory (EEPROM)
Electrically Erasable Programmable Read Only (EEPROM) memory gives the flexibility to re-program the same chip using electrical signals.
The information contained in the EEPROM memory can be altered by using electrical signals at the register/byte level.
They can be erased and reprogrammed within the circuit.
These chips include a chip erase mode and in this mode they can be erased in a few milliseconds.
It provides greater flexibility for system design.
The only limitation is their capacity is limited when compared with the standard ROM (A few kilobytes).

## Slide 9: Typical Embedded System
      Program Storage Memory – FLASH
FLASH memory is a variation of EEPROM technology.
It combines the re-programmability of EEPROM and the high capacity of standard ROMs.
FLASH memory is organized as sectors (blocks) or pages.
FLASH memory stores information in an array of floating gate MOSFET transistors.
The erasing of memory can be done at sector level or page level without affecting the other sectors or pages.
Each sector/page should be erased before re-programming.

## Slide 10: Typical Embedded System
      Memory – Read-Write Memory/Random Access Memory (RAM)
RAM is the data memory or working memory of the controller/processor.
RAM is volatile, meaning when the power is turned off, all the contents are destroyed.
RAM is a direct access memory, meaning we can access the desired memory location directly without the need for traversing through the entire memory locations to reach the desired memory position (i.e. Random Access of memory location).

## Slide 11: Typical Embedded System
      RAM – Static RAM (SRAM)
Static RAM stores data in the form of Voltage. They are made up of flip-flops.
In typical implementation, an SRAM cell (bit) is realized using 6 transistors (or 6 MOSFETs). Four of the transistors are used for building the latch (flip-flop) part of the memory cell and 2 for controlling the access.
Static RAM is the fastest form of RAM available. SRAM is fast in operation due to its resistive networking and switching capabilities.
SRAM cell implementation

## Slide 12: Typical Embedded System
      RAM – Dynamic RAM (DRAM)
Dynamic RAM stores data in the form of charge. They are made up of MOS transistor gates.
The advantages of DRAM are its high density and low cost compared to SRAM.
The disadvantage is that since the information is stored as charge it gets leaked off with time and to prevent this they need to be refreshed periodically.
Special circuits called DRAM controllers are used for the refreshing operation. The refresh operation is done periodically in milliseconds interval.
DRAM cell implementation

## Slide 13: Typical Embedded System
      RAM – SRAM Vs DRAM
SRAM | DRAM
Made up of 6 CMOS transistors (MOSFET) | Made up of a MOSFET and a capacitor
Doesn’t Require refreshing | Requires refreshing
Low capacity (Less dense) | High Capacity (Highly dense)
More expensive | Less Expensive
Fast in operation. Typical access time is 10ns | Slow in operation due to refresh requirements. Typical access time is 60ns. Write operation is faster than read operation.

## Slide 14: Typical Embedded System
      RAM – Non Volatile RAM (NVRAM)
Random access memory with battery backup.
It contains Static RAM based memory and a minute battery for providing supply to the memory in the absence of external power supply.
The memory and battery are packed together in a single package.
NVRAM is used for the non volatile storage of results of operations or for setting up of flags etc.
The life span of NVRAM is expected to be around 10 years.
DS1744 from Maxim/Dallas is an example for 32KB NVRAM.