## Slide 1: Embedded System Design
Unit II
Typical Embedded System
Mr. A. Chandra Shaker
Asst. Prof

## Slide 2: Typical Embedded System
Unit II
Core of Embedded System
Memory
Sensors and Actuators
Communication Interface

## Slide 3: Typical Embedded System
      Memory According to the Type of Interface
The interface (connection) of memory with the processor/controller can be of various types:
  Parallel interface (parallel data lines (D0-D7) of 8-bit processor/controller will be connected to D0-D7 of the memory)
  Serial interface (I2C - 2 line interface, SPI - 2+n line interface where n stands for total number of SPI bus devices in the system)
Serial interface is commonly used for data storage memory like EEPROM.
Memory density of a serial interface memory is usually expressed in terms of kilobits, whereas that of parallel interface memory is expressed in terms of kilobytes.
Atmel’s AT24C512 is an example for serial memory with capacity 512 kilobits and 2-wire interface.

## Slide 4: Typical Embedded System
      Memory Shadowing
From timing parameters, it is known that RAM access is about three times faster than ROM access.
Shadowing of memory is a technique adopted to solve the execution speed problem in processor-based systems.
In personal computer systems, BIOS stores the hardware configuration information. Usually it is read and system is configured according to it during system boot up which is time consuming.
Manufacturers included a RAM behind the logical layer of BIOS at its same address as a shadow to the BIOS. So during the boot up BIOS is copied to the shadowed RAM and RAM is write protected, then BIOS reading is disabled.

## Slide 5: Typical Embedded System
      Memory Selection for Embedded Systems
The memory requirement for an embedded system in terms of RAM and ROM is solely dependent on the type of embedded system and the applications for which it is designed.
Lot of factors need to be considered when selecting the type and size of memory for embedded system.
As a rule of thumb, identify your system requirement and based on the type of processor (SoC or a microcontroller with on-chip memory) used for the design, take a decision on whether the on-chip memory is sufficient or external memory is required.
If the embedded design is based on an RTOS, the RTOS requires certain amount of RAM for its execution and ROM for storing the RTOS image.

## Slide 6: Typical Embedded System
      Memory Selection for Embedded Systems
There are two parameters for representing a memory:
  Size of memory chip (Memory density expressed in terms of number of memory bytes per chip)
  Word size of memory (Word size refers to the number of memory bits that can be read/write together at a time)
Memory chips come in standard sizes like 512 bytes, 1024 bytes (1 kilobyte), 2048 bytes (2 kilobytes), 4 Kb, 8Kb, 16 Kb, 32 Kb, 64 Kb, 128 Kb, 256 Kb, 512 Kb, 1024 Kb (1 megabytes), etc. While you select a memory size, always keep in mind the address range supported by your processor.
Word sizes supported by memory chips are 4, 8, 12, 16, 24, 32, etc. Ensure that the word size supported by the memory chip matches with the data bus width of the processor/controller.