## Slide 1: Embedded System Design
Unit II
Typical Embedded System
Mr. A. Chandra Shaker
Asst.Prof

## Slide 2: Typical Embedded System
Unit II
Core of Embedded System
Memory
Sensors and Actuators
Communication Interface

## Slide 3: Typical Embedded System
      Sensors and Actuators
Sensor:
A transducer device which converts energy from one form to another for any measurement or control purpose. Sensors acts as input device.
Eg. Hall Effect sensor which measures the distance between the cushion and magnet in the Smart Running shoes from Adidas.
Actuator:
A form of transducer device (mechanical or electrical) which converts signals to corresponding physical action (motion). Actuator acts as an output device.
Eg. Micro motor actuator which adjusts the position of the cushioning element in the Smart Running shoes from Adidas.

## Slide 4: Typical Embedded System
      The I/O Subsystem
The I/O subsystem of the embedded system facilitates the interaction of the embedded system with external world.
The interaction happens through the sensors and actuators connected to the Input and output ports respectively of the embedded system.
The sensors may not be directly interfaced to the Input ports, instead they may be interfaced through signal conditioning and translating systems like ADC, Optocouplers etc.

## Slide 5: Typical Embedded System
      I/O Devices - Light Emitting Diode (LED)
Light Emitting Diode (LED) is an output device for visual indication in any embedded system.
LED can be used as an indicator for the status of various signals or situations. Typical examples are indicating the presence of power conditions like ‘Device ON’, ‘Battery low’ or ‘Charging of battery’ for a battery operated handheld embedded devices.
LED is a p-n junction diode and it contains an anode and a cathode. For proper functioning of the LED, the anode of it should be connected to +ve terminal of the supply voltage and cathode to the –ve terminal of supply voltage.
The current flowing through the LED must limited to a value below the maximum current that it can conduct. A resister is used in series between the power supply and the resistor to limit the current through the LED.

## Slide 6: Typical Embedded System
      I/O Devices - 7-Segment LED Display
The 7 – segment LED display is an output device for displaying alpha numeric characters.
It contains 8 light-emitting diode (LED) segments arranged in a special form. Out of the 8 LED segments, 7 are used for displaying alpha numeric characters.
The LED segments are named A to G and the decimal point LED segment is named as DP.
The LED Segments A to G and DP should be lit accordingly to display numbers and characters.
The 7 – segment LED displays are available in two different configurations, namely; Common anode and Common cathode.
In the Common anode configuration, the anodes of the 8 segments are connected commonly whereas in the Common cathode configuration, the 8 LED segments share a common cathode line.

## Slide 7: Typical Embedded System
      7-Segment LED Display
Based on the configuration of the 7 – segment LED unit, the LED segment anode or cathode is connected to the Port of the processor/controller in the order ‘A’ segment to the Least significant port Pin and DP segment to the most significant Port Pin.
The current flow through each of the LED segments should be limited to the maximum value supported by the LED display unit.
The typical value for the current falls within the range of 20mA.
The current through each segment can be limited by connecting a current limiting resistor to the anode or cathode of each segment.

## Slide 8: Typical Embedded System
      I/O Devices - Optocoupler
Optocoupler is a solid state device to isolate two parts of a circuit. Optocoupler combines an LED and a photo-transistor in a single housing (package).
In electronic circuits, optocoupler is used for suppressing interference in data communication, circuit isolation, High voltage separation, simultaneous separation and intensification signal etc.
Optocouplers can be used in either input circuits or in output circuits.
Optocoupler
Optocoupler in input and output circuit

## Slide 9: Typical Embedded System
      I/O Devices – Stepper Motor
Stepper motor is an electro mechanical device which generates discrete displacement (motion) in response to dc electrical signals.
It differs from the normal dc motor in its operation. The dc motor produces continuous rotation on applying dc voltage whereas a stepper motor produces discrete rotation in response to the dc voltage applied to it.
Stepper motors are widely used in industrial embedded applications, consumer electronic products and robotics control systems.
The paper feed mechanism of a printer/fax makes use of stepper motors for its functioning.
Based on the coil winding arrangements, a two phase stepper motor is classified into:
  Unipolar
  Bipolar

## Slide 10: Typical Embedded System
      Stepper Motor
Unipolar: A unipolar stepper motor contains two windings per phase. The direction of rotation (clockwise or anticlockwise) of a stepper motor is controlled by changing the direction of current flow. Current in one direction flows through one coil and in the opposite direction flows through the other coil. It is easy to shift the direction of rotation by just switching the terminals to which the coils are connected.
Bipolar: A bipolar stepper motor contains single winding per phase. For reversing the motor rotation the current flow through the windings is reversed dynamically. It requires complex circuitry for current flow reversal.

## Slide 11: Typical Embedded System
      2 Phase Unipolar Stepper Motor – Stator Winding

## Slide 12: Typical Embedded System
      2 Phase Unipolar Stepper Motor – Stepping Sequence
Full Step:
In the full step mode both the phases are energized simultaneously. The coils A, B, C and D are energized in the order.
Step | Coil A | Coil B | Coil C | Coil D
1 | H | H | L | L
2 | L | H | H | L
3 | L | L | H | H
4 | H | L | L | H
Only one winding of a phase is energized at a time.

## Slide 13: Typical Embedded System
      2 Phase Unipolar Stepper Motor – Stepping Sequence
Wave Step:
Only one phase is energized at a time and each coils of the phase are energized alternatively. The coils A, B, C and D are energized in the order.
Step | Coil A | Coil B | Coil C | Coil D
1 | H | L | L | L
2 | L | H | L | L
3 | L | L | H | L
4 | L | L | L | H
Only one winding of a phase is energized at a time.

## Slide 14: Typical Embedded System
      2 Phase Unipolar Stepper Motor – Stepping Sequence
Half Step:
Half step uses the combination of wave and full step. It has the highest torque and stability. The coils A, B, C and D are energized in the order.
Step | Coil A | Coil B | Coil C | Coil D
1 | H | L | L | L
2 | H | H | L | L
3 | L | H | L | L
4 | L | H | H | L
5 | L | L | H | L
6 | L | L | H | H
7 | L | L | L | H
8 | H | L | L | H
The rotation of the stepper motor can be reversed by reversing the order in which the coil is energized.

## Slide 15: Typical Embedded System
      2 Phase Unipolar Stepper Motor – Interfacing
Depending on the current and voltage requirements, special driving circuits are required to interface the stepper motor with microcontroller/processors.
Stepper motor driving ICs like ULN2803 or simple transistor based driving circuit can be used for interfacing stepper motors with processor/controller.