## Slide 1: Embedded System Design
Unit II
Typical Embedded System
Mr. A. Chandra Shaker
Asst. Prof.

## Slide 2: Typical Embedded System
Unit II
Core of Embedded System
Memory
Sensors and Actuators
Communication Interface

## Slide 3: Typical Embedded System
      I/O Devices – Relay
An electro mechanical device which acts as dynamic path selectors for signals and power.
The ‘Relay’ unit contains a relay coil made up of insulated wire on a metal core and a metal armature with one or more contacts.
‘Relay’ works on electromagnetic principle. When a voltage is applied to the relay coil, current flows through the coil, which in turn generates a magnetic field. The magnetic field attracts the armature core and moves the contact point. The movement of the contact point changes the power/signal flow path.

## Slide 4: Typical Embedded System
      Relay
The Relay is normally controlled using a relay driver circuit connected to the port pin of the processor/controller.
A transistor is used for building the relay driver circuit. The transistor can be selected depending on the relay driving current requirements.

## Slide 5: Typical Embedded System
      I/O Devices – Push Button Switch
Push Button switch is an input device.
Push button switch comes in two configurations, namely ‘Push to Make’ and ‘Push to Break’.
In the ‘Push to Make’ configuration, the switch is normally in the open state and it makes a circuit contact when it is pushed or pressed.
In the ‘Push to Break’ configuration, the switch is normally in the closed state and it breaks the circuit contact when it is pushed or pressed.
The push button stays in the ‘closed’ (For Push to Make type) or ‘open’ (For Push to Break type) state as long as it is kept in the pushed state and it breaks/makes the circuit connection when it is released.
Push button is used for generating a momentary pulse.

## Slide 6: Typical Embedded System
      I/O Devices – Keyboard
Keyboard is an input device for user interfacing.
If the number of keys required is very limited, push button switches can be used and they can be directly interfaced to the port pins for reading.
Matrix keyboard is an optimum solution for handling large number of key requirements.
Matrix keyboard greatly reduces the number of interface connections.
Matrix keyboard connects the keys in a row column fashion.
For example, for interfacing 16 keys, in the direct interfacing technique 16 port pins are required, where as in the matrix keyboard only 8 lines are required. The 16 keys are arranged in a 4 columns and 4 rows matrix.
The key press in matrix keyboard is identified with row-column scanning technique.

## Slide 7: Typical Embedded System
      Matrix Keyboard

## Slide 8: Typical Embedded System
      I/O Devices – Programmable Peripheral Interface (PPI)
Programmable Peripheral Interface (PPI) devices are used for extending the I/O capabilities of processors/controllers.
8255A is a popular PPI device for 8 bit processors/controllers.
8255A supports 24 I/O pins ad these I/O pins can be grouped as either three 8-bit parallel ports (Port A, Port B and Port C) or two 8 bit parallel ports (Port A and Port B) with Port C in any one of the following configurations.
    As 8 individual I/O pins
    Two 4bit Ports namely Port CUPPER (CU) and Port CLOWER (CL)
The Configuration of ports is done through the Control Register of 8255A.
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
Control Register

## Slide 9: Typical Embedded System
      Programmable Peripheral Interface (PPI)
Bit | Description | Bit | Description
D0 | Port C lower (CL) I/O mode selector D0 = 1; Sets CL as Input Port D0 = 0; Sets CL as Output Port | D4 | Port A I/O mode selector D4 = 1; Sets Port A as Input Port D4 = 0; Sets Port A as Output Port
D1 | Port B I/O mode selector D1 = 1; Sets Port B as Input Port D1 = 0; Sets Port B as Output Port | D5, D6 | Mode Selector for Port C upper and Port A D6 D5 = 00; Mode 0 – Simple I/O mode D6 D5 = 01; Mode 1 – Handshake Mode. Port A uses 3 bits of Port C as handshake signals D6 D5 = 1X; Mode 2. X can be 0 or 1 – Port A functions as Bi-directional Port
D2 | Mode Selector for Port C lower and Port B D2 = 0; Mode 0 – Port B functions as 8 bit I/O Port. Port C lower functions as 4 bit Port. D2 = 1; Mode 1 – Handshake Mode. Port B uses 3 bits of Port C as handshake signals | D7 | Control/Data mode selector for Port C D7 = 1; I/O mode. D7 = 0; Bit Set/Reset (BSR) mode. Functions as the control/status lines for Port A and B. The bits of Port C can be set or reset just as if they were output ports.
D3 | Port C Upper (CU) I/O mode selector D3 = 1; Sets CU as Input Port D3 = 0; Sets CU as Output Port |  | 

## Slide 10: Typical Embedded System
      Programmable Peripheral Interface (PPI) Interfacing