## Slide 1: Embedded System Design
Unit II
Typical Embedded System
Mr. A. Chandra Shaker
Asst. Prof.

## Slide 2: Typical Embedded System
Unit II
Core of Embedded System
Memory
Sensors and Actuators
Communication Interface

## Slide 3: Typical Embedded System

## Slide 4: Typical Embedded System
      Communication Interface
Communication interface is essential for communicating with various subsystems of the embedded system and with the external world.
For an embedded product, the communication interface can be viewed in two different perspectives; namely; Device/board level communication interface (Onboard Communication Interface) and Product level communication interface (External Communication Interface).
Embedded product is a combination of different types of components (chips/devices) arranged on a Printed Circuit Board (PCB).
The communication channel which interconnects the various components within an embedded product is referred as Device/board level communication interface (Onboard Communication Interface).

## Slide 5: Typical Embedded System
      Communication Interface
Serial interfaces like I2C, SPI, UART, 1-Wire etc and Parallel bus interface are examples of ‘Onboard Communication Interface’.
The ‘Product level communication interface’ (External Communication Interface) is responsible for data transfer between the embedded system and other devices or modules.
The external communication interface can be either wired media or wireless media and it can be a serial or parallel interface. Infrared (IR), Bluetooth (BT), Wireless LAN (Wi-Fi), Radio Frequency waves (RF), GPRS etc are examples for wireless communication interface.
RS-232C/RS-422/RS 485, USB, Ethernet (TCP-IP), IEEE 1394 port, Parallel port, CF-II Slot, SDIO, PCMCIA etc are examples for wired interfaces.

## Slide 6: Typical Embedded System
      On-board Communication Interface – I2C
Inter Integrated Circuit Bus (I2C - Pronounced ‘I square C’) is a synchronous bi-directional half duplex (one-directional communication at a given point of time) two wire serial interface bus.
The concept of I2C bus was developed by ‘Philips Semiconductors’ in the early 1980’s. The original intention of I2C was to provide an easy way of connection between a microprocessor/microcontroller system and the peripheral chips in Television sets.
The I2C bus is comprised of two bus lines, namely; Serial Clock – SCL and Serial Data – SDA.
SCL line is responsible for generating synchronization clock pulses and SDA is responsible for transmitting the serial data across devices.

## Slide 7: Typical Embedded System
      I2C
I2C bus is a shared bus system to which many number of I2C devices can be connected. Devices connected to the I2C bus can act as either ‘Master’ device or ‘Slave’ device.
The ‘Master’ device is responsible for controlling the communication by initiating/terminating data transfer, sending data and generating necessary synchronization clock pulses.
‘Slave’ devices wait for the commands from the master and respond upon receiving the commands.
‘Master’ and ‘Slave’ devices can act as either transmitter or receiver.
Regardless whether a master is acting as transmitter or receiver, the synchronization clock signal is generated by the ‘Master’ device only.
I2C supports multi masters on the same bus.

## Slide 8: Typical Embedded System
      I2C

## Slide 9: Typical Embedded System
      I2C
The sequence of operation for communicating with an I2C slave device is:
  Master device pulls the clock line (SCL) of the bus to ‘HIGH’.
  Master device pulls the data line (SDA) ‘LOW’, when the SCL line is at logic ‘HIGH’ (This is the ‘Start’ condition for data transfer).
  Master sends the address (7 bit or 10 bit wide) of the ‘Slave’ device to which it wants to communicate, over the SDA line. Clock pulses are generated at the SCL line for synchronizing the bit reception by the slave device. The MSB of the data is always transmitted first. The data in the bus is valid during the ‘HIGH’ period of the clock signal.
  Master sends the Read or Write bit (Bit value = 1 Read Operation; Bit value = 0 Write Operation) according to the requirement.
  Master waits for the acknowledgement bit from the slave device whose address is sent on the bus along with the Read/Write operation command. Slave devices connected to the bus compares the address received with the address assigned to them.

## Slide 10: Typical Embedded System
      I2C
  The Slave device with the address requested by the master device responds by sending an acknowledge bit (Bit value =1) over the SDA line.
  Upon receiving the acknowledge bit, master sends the 8bit data to the slave device over SDA line, if the requested operation is ‘Write to device’. If the requested operation is ‘Read from device’, the slave device sends data to the master over the SDA line.
  Master waits for the acknowledgement bit from the device upon byte transfer complete for a write operation and sends an acknowledge bit to the slave device for a read operation.
  Master terminates the transfer by pulling the SDA line ‘HIGH’ when the clock line SCL is at logic ‘HIGH’ (Indicating the ‘STOP’ condition).

## Slide 11: Typical Embedded System
      On-board Communication Interface – SPI
The Serial Peripheral Interface Bus (SPI) is a synchronous bi-directional full duplex four wire serial interface bus.
The concept of SPI is introduced by Motorola.
SPI is a single master multi-slave system. It is possible to have a system where more than one SPI device can be master, provided the condition only one master device is active at any given point of time, is satisfied.
SPI requires four signal lines for communication. They are:
  Master Out Slave In (MOSI): Signal line carrying the data from master to slave device. It is also known as Slave Input/Slave Data In (SI/SDI).
  Master In Slave Out (MISO): Signal line carrying the data from slave to master device. It is also known as Slave Output (SO/SDO).
  Serial Clock (SCLK): Signal line carrying the clock signals.
  Slave Select (SS): Signal line for slave device select. It is an active low signal.

## Slide 12: Typical Embedded System
      SPI

## Slide 13: Typical Embedded System
      SPI
The master device is responsible for generating the clock signal.
Master device selects the required slave device by asserting the corresponding slave device’s slave select signal ‘LOW’.
The data out line (MISO) of all the slave devices when not selected floats at high impedance state.
The serial data transmission through SPI Bus is fully configurable. SPI devices contain certain set of registers for holding these configurations.
The Serial Peripheral Control Register holds the various configuration parameters like master/slave selection for the device, baud rate selection for communication, clock signal control etc.
The status register holds the status of various conditions for transmission and reception.

## Slide 14: Typical Embedded System
      SPI
SPI works on the principle of ‘Shift Register’.
The master and slave devices contain a special shift register for the data to transmit or receive.
The size of the shift register is device dependent. Normally it is a multiple of 8.
During transmission from the master to slave, the data in the master’s shift register is shifted out to the MOSI pin and it enters the shift register of the slave device through the MOSI pin of the slave device.
At the same time the shifted out data bit from the slave device’s shift register enters the shift register of the master device through MISO pin.