## Slide 1: Embedded System Design
Unit II
Typical Embedded System
Mr. A. Chandra Shaker
Asst. Prof.

## Slide 2: Typical Embedded System
Unit II
Core of Embedded System
Memory
Sensors and Actuators
Communication Interface

## Slide 3: Typical Embedded System
      On-board Communication Interface – UART
Universal Asynchronous Receiver Transmitter (UART) based data transmission is an asynchronous form of serial data transmission.
The serial communication settings (Baud rate, No. of bits per byte, parity, No. of start bits and stop bit and flow control) for both transmitter and receiver should be set as identical.
The start and stop of communication is indicated through inserting special bits in the data stream.

## Slide 4: Typical Embedded System
      On-board Communication Interface – UART
While sending a byte of data, a start bit is added first and a stop bit is added at the end of the bit stream. The least significant bit of the data byte follows the start bit.
The ‘Start’ bit informs the receiver that a data byte is about to arrive. The receiver device starts polling its ‘receive line’ as per the baud rate settings.
If parity is enabled for communication, the UART of the transmitting device adds a parity bit.

## Slide 5: Typical Embedded System
      UART
The UART of the receiving device calculates the parity of the bits received and compares it with the received parity bit for error checking.
The UART of the receiving device discards the ‘Start’, ‘Stop’ and ‘Parity’ bit from the received bit stream and converts the received serial bit data to a word.