## Slide 1: Embedded System Design
Unit II
Typical Embedded System
Mr. A. Chandra Shaker
Asst. Prof.

## Slide 2: Typical Embedded System
Unit II
Core of Embedded System
Memory
Sensors and Actuators
Communication Interface

## Slide 3: Typical Embedded System
      On-board Communication Interface – 1-Wire Interface
An asynchronous half-duplex communication protocol developed by Maxim Dallas Semiconductor. It is also known as Dallas 1-Wire protocol.
It makes use of only a single signal line (wire) called DQ for communication and follows the master-slave communication model
The 1-Wire interface supports a single master and one or more slave devices on the bus.

## Slide 4: Typical Embedded System
      1-Wire Interface
The 1-Wire is capable of carrying power to the slave device apart from carrying the signals. Slave devices incorporate internal capacitor to generate power to operate the device from the 1-Wire.
Every 1-Wire device contains a globally unique 64 bit identification number stored within it. This unique identification number can be used for addressing individual devices present in the bus in case there are multiple slave devices connected to the 1-Wire bus.
The identifier has three parts: an 8 bit family code, a 48 bit serial number and an 8 bit CRC computed from the first 56 bits.

## Slide 5: Typical Embedded System
      1-Wire Interface

## Slide 6: Typical Embedded System
      1-Wire Interface
The sequence of operation for communicating with a 1-Wire slave device is:
  Master device sends a ‘Reset’ pulse on the 1-Wire bus.
  Slave device(s) present on the bus respond with a ‘Presence’ pulse.
  Master device sends a ROM Command (Net Address Command followed by the 64 bit address of the device). This addresses the slave device(s) to which it wants to initiate a communication
  Master device sends a read/write function command to read/write the internal memory or register of the slave device.
  Master initiates a Read data /Write data from the device or to the device

## Slide 7: Typical Embedded System
      On-board Communication Interface – Parallel Interface
Parallel interface is normally used for communicating with peripheral devices which are memory mapped to the host of the system.
The host processor/controller of the embedded system contains a parallel bus and the device which supports parallel bus can directly connect to this bus system.
The communication through the parallel bus is controlled by the control signal interface between the device and the host.

## Slide 8: Typical Embedded System
      Parallel Interface
The ‘Control Signals’ for communication includes ‘Read/Write’ signal and device select signal.
The device normally contains a device select line and the device becomes active only when this line is asserted by the host processor.
The direction of data transfer (Host to Device or Device to Host) can be controlled through the control signal lines for ‘Read’ and ‘Write’.
Only the host processor has control over the ‘Read’ and ‘Write’ control signals.

## Slide 9: Typical Embedded System
      Parallel Interface